## Slide 1: ECE 445S Real-Time Digital Signal Processing Lab Spring 2023 Infinite Impulse Response Filters
Prof. Brian L. Evans and Dan Jacobellis
Dept. of Electrical and Computer Engineering
The University of Texas at Austin
Lecture 6 http://users.ece.utexas.edu/~bevans/courses/realtime

## Slide 2: Outline
Comparison to FIR filters
  Moving average vs EWMA
IIR biquad filter structures
IIR filter design
Applications
  Chromagram
  Vocoder


X
O
O
X
IIR
FIR

## Slide 3: Discrete-Time Moving average
  Frequency response:
  Group Delay:

## Slide 4: Discrete-Time Moving Average

## Slide 5: Discrete-Time Moving Average
Group delay:

## Slide 6: Exponential Moving Average
  Frequency response:
Notes: ℎ[𝑛]=〖0.9〗^𝑛 𝑢[𝑛]
𝐻(𝑧)=1/(1−0.9𝑧^(−1) ), |𝑧|>0.9

## Slide 7: Exponential Moving Average

## Slide 8: Exponential Moving Average

## Slide 9: Discrete-Time IIR Filters
How to implement IIR filters?
  Output of LTI system is convolution with impulse response
  Impulse response is infinite in duration
  Cannot directly compute convolution sum
  Instead, use feedback to recursively compute the output

## Slide 10: Many Equivalent Representations
Difference equation

x[n]
y[n]
Unit Delay
0.9
y[n-1]
Pole at
Transfer function
  Assumes LTI system
Poles and zeros in z-plane
Recursive computation requires . For the filter to be LTI, .
Block diagram

## Slide 11: General Form of IIR Filter
  Feedback terms are subtracted so that correspond to denominator coefficients and correspond to numerator coefficients in transfer function

## Slide 12: First Order IIR filter
  Single zero at and a single pole at
  If coefficients are real, pole and zero locations are limited to real axis in the z-plane

x[n]
y[n]
x[n-1]
b1
b0
Unit Delay
a1
y[n-1]
Unit Delay
Notes: First order filter demo using matlab filterDesigner
Design method: IIR Butterworth Specify order 1
Units: normalized
Wc: 0.1
Design filter
Click pole-zero tab on left sidebar
Select poles and zeros and adjust magnitude
DSP first demos
https://dspfirst.gatech.edu/chapters/08feedbac/demos/3_domain/index.html

## Slide 13: Second Order (Biquad) IIR Filter
Biquad: short for biquadratic
  Transfer function is ratio of two quadratic polynomials
Direct form I

## Slide 14: Biquad in Direct form II
All-pole IIR Filter
x[n]
v[n]
FIR Filter
y[n]
All-pole IIR filter
FIR Filter

## Slide 15: Second Order (Biquad) IIR Filter
  Example: bandstop filter
Biquad poles and zeros
  If coefficients are real, then poles and zeros will be complex conjugate pairs
  Allowing complex poles and zeros provides more flexibility for designing filters compared to single order IIR filter

## Slide 16: Vocoder
  Instead of representing speech by signal amplitude, represent based on filter parameters
“Voice Encoder”
  Originally developed for speech synthesis and for encoding speech for telecommunications
  Video: speech synthesis (1939)
  Use as a musical effect (lab #7)
Source-Filter model of speech production
  Opening and closing of vocal folds produces many harmonically related frequencies
  Model vocal tract (including lips, teeth, etc) as LTI filter
  Poles are especially important since they model resonances

## Slide 17: Chromagram
Map audio signal to notes
  Musical notes are perceived as similar when their frequencies differ by an octave (factor of 2)
  12-tone equal temperament divides each octave into 12 bins:
  {C, C♯, D, D♯, E , F, F♯, G, G♯, A, A♯, B}
  MATLAB code (PDF, piano.wav)
Use bank of IIR filters to extract each note
  IIR filters provide much better frequency selection than FIR
  Less delay on average compared to FIR
  Only average energy is displayed, nonlinear phase is okay

## Slide 18: IIR Biquad Frequency Responses
Magnitude response
  Zeros z0 & z1 and poles p0 & p1
  |a – b| is distance between complex numbers a and b
  |ej – p0| is distance from point on unit circle ej and pole p0
IIR Biquad Filter Structures

## Slide 19: Frequency Response?
zeroAngle = 15*pi/16;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/16;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]’) / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
X
O
O
X
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
z0 = exp(j*zeroAngle);
z1 = exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 0.9;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Re(z)
Im(z)
O
O
X
X
zeroAngle = pi/4;
rz = 1/0.8;
z0 = rz*exp(j*zeroAngle);
z1 = rz*exp(-j*zeroAngle);
numer = [1 -(z0+z1) z0*z1];
r = 1/rz;
poleAngle = pi/4;
p0 = r * exp(j*poleAngle);
p1 = r * exp(-j*poleAngle);
denom = [1 -(p0+p1) p0*p1];
%%% Normalize the DC response
%%% to 1 in linear units by
%%% setting H(z) evaluated
%%% at z = 1 to be 1
C = (denom * [1 1 1]') / (numer * [1 1 1]');
freqz(C*numer, denom);
Lowpass, highpass, bandpass, bandstop, allpass, notch?
Poles have radius r Zeros have radius 1/r
Zeros are on the unit circle
handout

## Slide 20: Demonstrations
DSP First, 2nd ed., ch. 10
  IIR filtering tutorial (Link)
  Connection between the Z and frequency domains (Link)
  Time/frequency/z domain movies for IIR Filters (Link)
link
IIR filter with one pole and a zero at the origin
Movement of Poles
IIR Biquad Filter Structures

## Slide 21: Stability
A discrete-time LTI system is bounded-input bounded-output (BIBO) stable if for any bounded input x[n] such that | x[n] |  B1 < , then the filter response y[n] is also bounded | y[n] |  B2 < 
handout
Proposition: A discrete-time filter with an impulse response of h[n] is BIBO stable if and only if
  Every finite impulse response LTI system (even after implementation) is BIBO stable
  A causal infinite impulse response LTI system is BIBO stable if and only if its poles lie inside the unit circle
Stability

## Slide 22: BIBO Stability
Rule #1: For a causal sequence, poles are inside the unit circle (applies to z-transform functions that are ratios of two polynomials) OR
pole at z=a
Rule #2: Unit circle is in the region of convergence. (In continuous-time, imaginary axis would be in region of convergence of Laplace transform.)
Example:
  Stable if |a| < 1 by rule #1 or equivalently
  Stable if |a| < 1 by rule #2 because |z|>|a| and |a|<1
Stability

## Slide 23: Equalization
Design equalizer to compensate frequency distortion
x[m]
System Model (Filter)
LTI
h[m]
y[m]
Equalizer
LTI
g[m]
  Applications: Audio, image and communication systems
  Goal: Make cascade all-pass:
Example: H(z) is an FIR filter
Re(z)
Im(z)
  Zeros of H(z) become poles of G(z)
  Stability issues?
O
O
O
O
O
X
X
X
X
X
all-pass
notch
notch
cancellation
cancellation
Stability

## Slide 24: IIR Filter Design
Classical IIR filter design algorithms
Design Method | Passband | Stopband
Butterworth | Monotonic | Monotonic
Chebyshev type I | Monotonic | Ripples
Chebyshev type II | Ripples | Monotonic
Elliptic | Ripples | Ripples
Manual placement of poles and zeros
Cascade of Biquads
Automated adaptation of pole and zero locations
  Center frequency of bandpass resonator HW 1.1(d) & 2.1(d)
  Notch filter with parameterized notch frequency HW 3.1(c)

## Slide 25: IIR Filter Implementation
Cascade of biquads for N poles
  N even: N/2 conjugate pairs of poles. Cascade of N/2 biquads.
  N odd: One real pole and (N-1)/2 conjugate pairs of poles. Cascade of first-order filter (real pole) and (N-1)/2 biquads
  For M biquads, M! orderings of conjugate pairs of poles and for each ordering, M! orderings of conjugate pairs of zeros
  Exhaustive search: simulate all combinations to pick best one
  Quick pairing: Order biquads in ascending order of quality factors (see next slide) and for each each biquad, choose the conjugate zero pair that is closest in Euclidean distance
Single section (single difference equation)
  Could make a BIBO stable filter become BIBO unstable
Cascade of Biquads

## Slide 26: Quality Factors for Digital Biquads
For poles at a ± j b = r e ± j , where is pole radius (r < 1 for stability), with y = –2 a:
Filter design programs use r as approximation of quality factor
  Real poles: b = 0 and 1 < a < 1, so r = |a| and y = 2 a and Q = ½ (impulse response is C0 an u[n] + C1 n a n u[n])
  Poles on unit circle: r = 1 so Q =  (oscillatory response)
  Imaginary poles: a = 0 so r = |b| and y = 0, and
  Processors with 16-bit x 16-bit multipliers and 40-bit accumulators: Qmax  40
Cascade of Biquads
Measures sensitivity in pole locations to perturbations

## Slide 27: Quality Factors for Analog Biquads
Second-order filter section
  Conjugate symmetric poles a ± j b, where a < 0
  With no zeros, impulse response is
  which is pure decay when b = 0 and pure sinusoid when a = 0
Quality factor: measures sensitivity of pole locations to perturbations
  Real poles: b = 0 so Q = ½ (exponential decay response)
  Imaginary poles: a = 0 so Q =  (oscillatory response)
  Maximum Q values: 25 for board-level RC circuits, 40 for switched capacitor designs, and 80 for analog IC designs
Classical designs have biquads with high Q factors
Cascade of Biquads

## Slide 28: IIR Filter as Single Section
IIR filters have rational transfer functions
Direct form realization
  Dot product of vector of N +1 coefficients and vector of current input and previous N inputs (FIR section)
  Dot product of vector of M coefficients and vector of previous M outputs (“FIR” filtering of previous output values)
  Computation: M + N + 1 multiply-accumulates (MACs)
  Memory: M + N words for previous inputs/outputs and M + N + 1 words for coefficients
Common IIR Filter Structures

## Slide 29: IIR Filter as Single Section

x[n]
y[n]
y[n-M]
x[n-1]
x[n-2]
b2
b1
b0
Unit Delay
Unit Delay
Unit Delay
x[n-N]
bN
Feed-forward
a1
a2
y[n-1]
y[n-2]
Unit Delay
Unit Delay
Unit Delay
aM
Feedback
M and N may be different
Full Precision Wordlength of y[0] is 2 words. Wordlength of y[n] increases with n for n > 0.
Common IIR Filter Structures

## Slide 30: Stability As Single Section
IIR filter design to meet a specification
  Manual or automatic placement of poles and zeros
  Poles are inside unit circle for stability
Factored transfer function in poles, zeros and gain
  Expanded to obtain coefficients for difference equation
  Expansion for feedback coefficients can lead to instability
Second-order example: zeros z0 & z1, poles p0 & p1
  Each addition and multiplication in 64-bit floating point
worst-case loss of one bit
worst-case loss of 53 bits

## Slide 31: Stability As Single Section

## Slide 32: MATLAB Filter Designer Demo #1
Filter design/analysis
Lowpass filter design specification (all demos)
  fpass = 9600 Hz
  fstop = 12000 Hz
  fsampling = 48000 Hz
  Apass = 1 dB
  Astop = 80 dB
Under analysis menu
  Show magnitude, phase and group delay responses
FIR filter – equiripple
  Also called Remez Exchange or Parks-McClellan design
  Minimum order is 50
  Change Wstop to 80
  Order 100 gives Astop 100 dB
  Order 200 gives Astop 175 dB
  Order 300 does not converge –how to get higher order filter?
FIR filter – Kaiser window
  Minimum order 101 meets spec
Cascade of Biquads

## Slide 33: MATLAB Filter Designer Demo #2
IIR filter – elliptic
  Use second-order sections
  Filter order of 8 meets spec
  Achieved Astop of ~80 dB
  Poles/zeros separated in angle
  Zeros on or near unit circle indicate stopband
  Poles near unit circle indicate passband
  Two poles very close to unit circle but still BIBO stable
  Show group delay response
IIR filter – elliptic
  Use second-order sections
  Increase filter order to 9
  Eight complex symmetric poles and one real pole:
  Same observations on left
Cascade of Biquads

## Slide 34: MATLAB Filter Designer Demo #3
IIR filter – elliptic
  Use second-order sections
  Increase filter order to 20
  Two poles very close to unit circle but BIBO stable
Single section (Edit menu)
  Oscillation frequency ~9 kHz appears in passband
  BIBO unstable: two pairs of poles outside unit circle
IIR filter design algorithms return poles-zeroes-gain (PZK format): Impact on response when expanding polynomials in transfer function from factored to unfactored form (see slide 6-25)
Cascade of Biquads

## Slide 35: MATLAB Filter Designer Demo #4
IIR filter - constrained least pth-norm design
  Use second-order sections
  Limit pole radii ≤ 0.92
  Order 8 does not meet both passband/stopband specs for different weights
Filter order might increase but worth higher complexity for being more robust perturbations in pole locations
  Order 9 does indeed meet specs using Wpass = 1.5 and Wstop = 800
Cascade of Biquads

## Slide 36: Conclusion
 | FIR Filters | IIR Filters
Implementation complexity (1) | Higher | Lower (sometimes by factor of four)
Minimum order design algorithm | Parks-McClellan (Remez exchange) algorithm (2) | Elliptic design algorithm
BIBO stable? | Always | May become unstable when implemented (3)
Linear phase | If impulse response is symmetric or anti-symmetric about midpoint | No, but phase may made approximately linear over passband (or other band)
(1) For same piecewise constant magnitude specification (2) Algorithm to estimate minimum order for Parks-McClellan algorithm by Jim Kaiser may be off by 10%. Search for minimum order is often needed. (3) Choice of IIR filter structure matters -- use cascade of biquads instead of a single section. Some IIR filter design algorithms can constrain pole locations.

## Slide 37: Conclusion
Keep poles computed by filter design algorithms
  Polynomial deflation (rooting) reliable in floating-point
  Polynomial inflation (expansion) may degrade roots
Direct form IIR structures expand zeros and poles
  May become unstable for large order filters (order > 12) due to degradation in pole locations from polynomial expansion
Cascade of biquads (second-order sections)
  Only poles and zeros of second-order sections expanded
  Biquads placed in order of ascending quality factors
  Optimal ordering of biquads requires exhaustive search and each ordering can be simulated in parallel for speed